## Slide 1: OOI Data Quality Procedures and Tools
M. Vardaro, M. Crowley, L. Belabbassi, L. Garzio, J. Kerfoot, F. Knuth, S. Lichtenwalner, M. Smith
Rutgers University, New Brunswick, NJ
Notes: This is the entire Rutgers team

## Slide 2: Overview
Data Flow & Products
Data Review Procedures
Periodic Reviews & Documentation
Next Steps
Conclusions

## Slide 3
OOI By the Numbers
Arrays
Stable Platforms
Moorings, Profilers, Nodes
Mobile Assets
Gliders, AUVs
Instruments (~850 deployed)
Science Data Products
Science/Engineering Data Products
7
57
31
1227
>2500
>100K

## Slide 4
OOI: Web Portals
Main
OOINet
ERDDAP
Education
Shipboard Data
QC Database

## Slide 5: Data Flow Chart
Data types:
Telemetered Data
Recovered Data
Streamed Data
Shipboard Data
Metadata (CF 1.6)
Data product levels:
Raw, L0, L1, L2

## Slide 6: OOI Data Product Levels
Raw data: The datasets as they are received from the instrument
  May contain multiple L0, L1, or L2 parameters, data for multiple sensors, and be in native sensor units
  Always persisted and archived by the OOI
  Example: format 0 binary file from an SBE-37IM on a Global Flanking Mooring.
Level 0 (L0): Unprocessed, parsed data parameter that is in instrument/sensor units and resolution
  Sensor by sensor (unpacked and/or de-interleaved) and available in OOI supported formats (e.g., NetCDF)
  Always persisted and archived by the OOI
  Example: SBE-37IM Temperature portion of the hex string
Level 1 (L1): Data parameter that has been calibrated and is in scientific units
  Created on-demand via user synchronous or asynchronous request
  Actions to transform Level 0 to Level 1 data are captured and presented in the metadata of the Level 1 data
  Example: SBE-37IM Temperature converted from hex to binary and scaled to produce degrees C
Level 2 (L2): Derived data parameter created via an algorithm that draws on multiple L1 data products
  Created on-demand via user synchronous or asynchronous request
  Products may come from the same or separate instruments; data from all instruments are provided during download
  Example: SBE-37IM Density and Salinity
Notes: If an algorithm uses data streams from multiple instruments to produce L2 products, data from all relevant instruments will be provided during download

## Slide 7: OOI Data Status
All available telemetered and recovered data are being ingested and made accessible for download
Rutgers CI currently storing >340TB of raw data, including ~100 TB HD video (so video ≈ 30% of total data)
  ~150TB are publicly available via the raw data archive
  ~14TB of processed data ready for product generation
All known issues have been annotated. Unless otherwise remarked, the data have not been validated against in situ samples taken by instrumentation external to the system.

## Slide 8: Overview
Data Flow & Products
Data Review Procedures
Periodic Reviews & Documentation
Next Steps
Conclusions

## Slide 9: Data Team Primary Goals
Monitor the operational status of data flowing through the OOI system
Ensure the availability of OOI datasets in the system (raw, processed, derived, and cruise)
Ensure that data delivered by the system meets quality guidelines
Report operational statistics on data availability, data quality, and issue resolution

## Slide 10
Build Ingest Automation
Set up Recurring Ingestion
Ingest Missing Data
Download Plot Check Data
Make Annotations
Answer Questions
Instrument Pages
Tutorials
Create UI Issue Tickets
Create Data Issue Tickets
Suggest New UI Features
TestFixes and New Features
Produce Daily Resolution
Monitor Real-time Ingestion
Monitor Raw Data Delivery
Parse MIO Operational Stats
Data Team Tasks
Ingestion
CI Data Review
Helpdesk
UI Testing
Stats
Environmental and Raw Data Review
Data Team Portal
Compare to CI Output
Run Raw in Vendor Software
Data Availability Timelines
Display Daily Stats
Asset Mgmt Updates
Processes Environmental Data
Workshops
Conferences Publications
Fix QC Algorithms
Compare to CI Output
ERDDAP
Set up Front End
Set up Back End
Ingest Data
2018 Early Career Workshops

## Slide 11: OOI Automated QC Procedures
6 automated QC algorithms can produce 7 flags (including logical “or” which combines flags) which are plottable and are included in downloaded files
Coded based on specifications written by OOI Project Scientists, derived from QARTOD manuals and other observatory experiences
Algorithms refer to “lookup tables” assembled by OOI Project Scientists with input from subject matter experts: https://github.com/ooi-integration/qc-lookup
Global Range Test
Local Range Test
Spike Test
Stuck Value Test
Trend Test
Temporal Gradient Test
Spatial Gradient Test (Profile)

## Slide 12: NetCDF QC flags
NOTE: Results of the QC tests do not remove data.
Each parameter in a file has a corresponding *_qc_executed and *_qc_results variable
  qc_executed indicates which tests were run
  qc_results denotes which tests passed
Integer values can be converted to a binary that indicates which tests were run (1) or not (0), and which passed (1) or failed (0).
See example QC Python notebook or online guide (http://oceanobservatories.org/knowledgebase/interpreting-qc-variables-and-results/) for more details.

## Slide 13: Data Status Categories
Status | Description | QARTOD Code | QARTOD Description | Color
NOT_OPERATIONAL | Instrument not functional (no data expected) |  | Not operational | 
NOT_AVAILABLE | Instrument functional, data lost in transmission | 9 | Missing data | 
PENDING_INGEST | Instrument functional, data exists, Awaiting ingest |  |  | 
NOT_EVALUATED | Instrument functional, data exists, Awaiting evaluation | 2 | Not evaluated, not available or unknown | 
SUSPECT | Instrument functional, data exists and either failed a QC test or does not reflect environmental conditions | 3 | Questionable/suspect | 
FAIL | Instrument functional, data exists but is known to be bad due to known instrument or calibration error | 4 | Bad | 
PASS | Instrument functional, data exists, passed QC tests, is complete and looks reasonable | 1 | Good | 
GOOD | Instrument functional, data exists, passed QC tests, is complete and has undergone validation with shipboard datasets and reached the highest level of QC that the OOI can provide |  |  | 

## Slide 14: Data Annotation
Annotations are the primary means of communication between data team and users
Annotations can be directly entered via the GUI for specified data streams
Annotation text appears in a tab on the data catalog/plotting page
Annotation time ranges can be shown on plots (via “Options” interface)
Annotations also included in downloaded data

## Slide 15: Overview
Data Flow & Products
Data Review Procedures
Periodic Reviews & Documentation
Next Steps
Conclusions

## Slide 16: Reviews and Reporting
Quality Timeline
Annotation Text

## Slide 17: QC Database Tool (ooi.visualocean.net)
    Used for reference & statistics
    Includes status information, as well as a cruise data checklist
    Includes testing/review capability
    Annotation options

## Slide 18: Data Availability
QC Database: ooi.visualocean.net

## Slide 19: Examples of QC Effort
Pressure offsets
(Bad cal values)
Drift
Biofouling
Damage
Video issues

## Slide 20: Deliverables
Data Availability Reports
  (% completeness, streams/parameters reported, particles in the system)
Data Quality Reports
Redmine reporting
  Issues found, investigations, and Help Desk open/closed
Deep dive investigation reports
Annotations (to users)
Download statistics

## Slide 21: Overview
Data Flow & Products
Data Review Procedures
Periodic Reviews & Documentation
Next Steps (into 2.0)
Conclusions

## Slide 22: Data Availability and Completeness
Some derived data products are still being added to the system
Some products are available but do not show up in data catalog or cannot be plotted
Some products require additional processing (e.g. ZPLSC, HYDBB)
Seafloor Uplift and Deflation Mean Depth (BOTSFLU L2)
Seafloor Uplift and Deflation 10-min Rate of Depth Change (BOTSFLU L2)
Seafloor Uplift and Deflation
5-min Rate of Depth Change (BOTSFLU L2)

## Slide 23: Adding capability to OOINet experience
Notes: Improved bathymetry, better data download, increased asset management data

## Slide 24: Science Evaluation: Are ocean features encountered real? Outside local range
Is this real?
IOOS data shows presence
of warm core ring
Taking advantage of all assets, even non-NSF, to assess data quality
IOOS data shows ocean response to storm

## Slide 25: Vicarious Calibration - Comparisons enabled by ERDDAP
Glider 387
Comparison Segment
Concurrent profiles from Glider 387 and Coastal Pioneer Profiler Mooring
Co-located and concurrent Temperature and Salinity Profiles
Blue – Glider 387 Red – Coastal Pioneer Profiler Mooring

## Slide 26: Community Datasets & Tools
http://oceanobservatories.org/community-tools/
De-tided Bottom Pressure Recorder (BOTPT) data
W. Chadwick (OSU/CIMRS)
Student-collated biology catalog from Axial Seamount, using ROV and HD video records
D. Kelley (UW) & L. Sautter (Charleston)
Time-lapse videos of vent dynamics at Axial Seamount, using HD Video data
A. Marburg (UW/APL), T. Crone (LDEO) & F. Knuth (Rutgers)

## Slide 27: Partnerships
IRIS
NANOOS
NDBC
Notes: https://gliders.ioos.us/map/

## Slide 28: CI Priorities (Transition to 2.0)
Data product creation: Hydrophone data, Osmosampler, pCO2 Flux, VADCP, interpolation issues
Data discovery: navigation of data catalog, missing pressure data, image galleries, stream name consistency
User experience: login fixes, interpolated plots, data download issues (missing status, provenance errors), status indicators and dashboard, addition of multiple-stream download
Quality control: data displayed outside deployment time range, QC lookup values, fill value support, improved annotations

## Slide 29: Overview
Data Flow & Products
Data Review Procedures
Periodic Reviews & Documentation
Next Steps
Conclusions

## Slide 30: Conclusions
  A large amount of high quality data continues to be collected
  Data review is the primary focus, given maturation of the system and control over data ingestion
  Data team accelerating review via development of specialized tools
  Short-term goals for improving data quality and delivery (medium- and long-term goals are now recommendations for OOI 2.0)
  OOI is providing a curated, consistent data system delivering data and metadata to the community

## Slide 31
Leila Belabassi
Sage Lichtenwalner
Mike Smith
Friedrich Knuth
Lori Garzio
Mike Vardaro
Mike Crowley
John Kerfoot
Rutgers Data Team

## Slide 32: Questions?
OOI Main Web site: http://oceanobservatories.org
Data Portal: http://ooinet.oceanobservatories.org
Help Desk: help@oceanobservatories.org
Mike Vardaro, Data Manager, OOI CI Data Team
vardaro@marine.rutgers.edu
Mike Crowley, Program Manager, OOI CI Data Team
crowley@marine.rutgers.edu
Acknowledgements: NSF, COL, Rutgers University, University of Washington, WHOI, Oregon State University, Raytheon

## Slide 33: Supplemental Slides

## Slide 34
OOI Operations:
12.5 FTEs
OOI Management:
1.0 FTE
Leadership & Oversight: 0 FTE
Software Team Manager
Bill Kish
Data Evaluator
Friedrich Knuth
CI PI
Manish Parashar
Program Management
Data Manager
Mike Vardaro
Science PM
RU – Mike Crowley
Science/User PI
Scott Glenn
Leadership
&
Oversight
Software Configuration & Maintenance
Janeen Pisciotta
Data Team
Data Evaluator
Mike Smith
Software Team
Asst. Data Manager Leila Belabbassi
Data Evaluator
Lori Garzio
IT Manager
Juan José Villalobos
System Team
Technical Help Desk & Education-Outreach
Sage Lichtenwalner
User Services Team
System Engineering PM
RU – Ivan Rodero
Project Coordinator
Caroline McHugh
Science/User PI
Oscar Schofield
System Administrator
Aamir Jadoon
Software Test Eng.
Mark Steiner
Network Engineer
Jim Housell
RDI2
COOL
Rutgers CI Team
ERDDAP +
John Kerfoot
(ECR 1300-00525)
OOI Management:
1.0 FTE
(ECR 1300-00525)
Notes: ECR 1300-00525 funded Rodero/Crowley an additional 0.25 FTE each, Kerfoot approximately .5 FTE

## Slide 35: First in Class Reviews: Jan-Aug 2016
    One example of each data stream (ingestion completed by Systems team)
    Review of 1207 (467 science) streams completed in August 2016
    Tested parsers, algorithms, ingestion, asset management and data product creation

## Slide 36: Rest in Class Data Review Workflow
M2M Request
Automated tests
Plot Data File
Instrument Level
Deployment time range
Stream Level
Start and End Date
Lat/Lon
Duplicate Timestamps
Parameter Availability
Visual Assessment
Data Availability
Data Quality
Summary Report
Parameter Level
Global range
Stuck Value
Spike Test
Fill values
NaNs
Gap Check
Annotate in GitHub
Subsite – Operational Status
Node – Operational Status
Instrument – Operational Status
Stream - Availability
Parameter – Quality & Availability
Push to System
Investigate Gaps
and QC failures

## Slide 37: QARTOD/OOI QC Comparison
OOI Test | OOI Description | QARTOD Equivalent | QARTOD Recommendation (from manuals) | Notes
Global Range Test | Data are flagged unless they fall within valid world ocean ranges or instrument limits | Gross Range | Only considers manufacturer-defined sensor and calibration limits | Different tests, different names. Currently operational.
Spike Test | Deviation from mean compared to 2*N neighboring points | Spike | N=1, default threshold is based on the rate of change distribution from previous data sets | Roughly identical, same nomenclature. Currently operational.
Stuck Value Test | If 2 neighboring values differ by less than the resolution of the sensor for more than N repetitions, data are flagged | Stuck Sensor | Manual suggests 3 consecutive points for a stuck sensor suspect flag and 5 for a fail flag. | QARTOD manual suggestion may be too low for well-mixed portions of the water column. Under evaluation.
Local Range Test | Data are flagged unless they fall within locally valid site-specific or depth ranges. Interpolates thresholds between depth and season intervals | Local Range | Starts with constant limits for each depth/season interval | Roughly identical, same nomenclature. OOI Local ranges are still being established.
Gradient Test | If d(data)/d(t) > a set threshold, following points fail until one falls within limit (TOLDAT). First data point assumed good unless “good” starting data (STARTDAT) point is defined. | Rate of Change | QARTOD recommends two neighboring points and does not incorporate TOLDAT or STARTDAT values. | Different tests, different names. Under Evaluation, not operational
Trend Test | Data flagged as having trend if the SD of the residuals to a polynomial curve < original data, multiplied by a factor. Test for sensor drift. | N/A | No QARTOD equivalent | OOI only. Under Evaluation, not operational

## Slide 38: Quick Plots and Data Download

## Slide 39: Data Evaluation Daily Activities
Review the end-to-end operational status of online instruments and investigate any outages (e.g. instrument, telemetry, parsing, or ingestion failures).
Review the operational status of other data archives (raw, cruise, ERDDAP)
Look into and resolve new system alerts
Follow up on any issue requests from users (via Redmine)
Add annotations to notify users of operational status changes

## Slide 40: Daily Review Workflow
= Questions
= Actions
= Decision points
Notes: Add legend “The Legend of the Data Team”

## Slide 41: QC Challenges & Solutions
Local range values need statistical analysis of environmental data for each platform
  Need to work with SMEs to analyze and apply ranges and test algorithm
Trend test may not work as designed, because it requires the system to compare data prior to the user request date – analysis ongoing
Gradient test is complicated to apply, requires 2D dataset – analysis ongoing
Spike test is currently very simple - needs tweaking to avoid false positives/negatives (especially in biological data) and to work with certain data types
Not all QC algorithms apply to all data products – ongoing review with SMEs
The QC algorithms do NOT trigger alerts in the system - Alerts/alarms only trigger when new data is telemetered/streamed
  Can set alerts on L1/L2 data streams based on Global/Local range values

## Slide 42: Machine-to-Machine RESTful API
Raw data, metadata, & calibration values extracted on demand, algorithms applied
NetCDF data/metadata always the full time range requested, assembled once data products are created (asynchronous)
Synchronous JSON requests decimated down to a maximum of 20,000 data points
JSON response is instantaneous, making it useful for real-time plotting applications
Notes: Python, Matlab, R – any type of code. Requires authentication via UI, unlike some other systems.

## Slide 43
OOI ERDDAP
Current ERDDAP Status
1655 streams available
Telemetered, currently deployed systems
Data available via uFrame
Future Updates
Additional telemetered data sets updated as deployed
Cabled Array data
Recovered data (requires additional storage)
Multidimensional dataset issues
https://erddap-uncabled.oceanobservatories.org/uncabled/erddap/index.html
Notes: ERDDAP – API with no authentication or async download, familiar metadata format, plotting options, multiple data download formats

## Slide 44: Current “Rest-in-Class” Reviews
Process:
Check all deployments for presence & absence of all parameters
Check science parameters for reasonableness
Problem? Deep dive, report in Redmine, track, give feedback, check fixes, create annotations in QC Database
Challenge:
Automated tools, Redmine questions, Cal sheets, raw data repository, modify ingest CSVs, testing UI fixes
Upload and ingestion of data
Delivery and archiving of Cruise Data
Quality Assurance vs. Quality Control
Expediting the Solution:
Populate QC database to automatically check for presence/absence, gaps > 1 day, NaNs, negative values
Asset Management
(MIOs & Data Team)
Complete?
Correct?
2. Data Delivery & Ingestion
(MIOs, Systems, Data Team)
Includes Cruise Data
3. Data Review
Availability
Quality
4. Investigate Gaps and QC failures
5. Communicate Issues (Annotation)
Notes: CTDs (275) will be reviewed first, followed by fluorometers (148) and oxygen sensors (140). The next set of instruments will be reviewed in late 2017.
Photosynthetically active radiation (PAR), ADCPs, bulk meteorology (METBK), nitrate (NUTNR) and pH instruments are high on the list, as they are priority data sets for the community.

## Slide 45: Options for Data Review Acceleration
Option | Positive | Negative
MIO Operations Log at Rutgers | Centralized log reduces time spent investigating issues All issues entered consistently | Takes time to maintain Some development time
Speed up ingestion | Fewer gaps to investigate | Currently requires FTE Automated process not yet delivered
Data Team works only on RIC | More data reviewed faster | No new data in system No bug investigation No QA testing
Limit reviewed time period or stream type | Data reviewed slightly faster, at high level | Review enhanced by looking at multiple deployments and trends Slows down future reviews
Limit thoroughness of reviews | Data reviewed faster, at high level | Unclear why gaps exist Quality issues not fully annotated Slows down future reviews Limits crowdsourcing options
Crowdsourcing (enlist volunteer SMEs) | Removes subset of datasets from review queue Assistance with complex data that requires expertise | Focus on specific interest, not whole of OOI Steep learning curve for advanced use of system (and knowledge of known issues) Pathway to triage and incorporate feedback
Add employees or Data Assembly Center (DAC) | Data reviewed faster, in depth Support for expert analysis | Requires additional funding Setup and maintenance time
Notes: Indicate the different endgames: improve amount of data? Or produce a useful data product?

## Slide 46: Periodic Data Team Activities
Meet with MIOs to discuss operational issues and data quality
Instrument, stream, parameter and deployment completeness
Conduct deep dives on datasets to review availability and quality
Review & annotate full deployment data to assess data quality
Develop new scripts, plotting tools, and quality checks
Produce reports on the availability and quality of datasets
Review appropriateness of QC flags
Ensure asset, deployment, calibration, and ingestion configurations have been updated, and reports posted following every cruise
Prototype and test new user interface and visualization features